## Slide 1: DRAGen – Discrete RVE Automation and Generation
DRAGen – Beta Release Event
M. Henrich M.Sc., Niklas Fehlemann M.Sc., Orkun Karagüllü M.Sc., Maximilian Neite M.Sc.

## Slide 2: Introduction – Why DRAGen?
RVEs “should contain enough information on the microstructure yet be sufficiently smaller than the macroscopic structural dimensions. Thus, a separation of scales should be enabled” [1].
Dream3D supports:
Grain-shape and -size reconstruction
Texture reconstruction
Voxelmesh is standard, laplace smoothing available
Neper supports:
Grain size reconstruction with voronoi
Grain shape reconstruction with Aspectratio distribtion (experimental state)
Texture reconstruction including substructures
DRAGen supports:
Coupled Grain size and shape reconstruction based on Neural Networks
Texture reconstruction including substructure
Band reconstruction of secondary phase
Inclusion reconstruction
Laplace smoothed Hex-mesh is standard, (Voxelmesh available)
Surface Roughness
[1] Gitman, I.M.; Askes, H.; Sluys, L.J. Representative volume: Existence and size determination. Eng. Fract. Mech. 2007, 74, 2518–2534.

## Slide 3: DRAGen – The Main Idea
Microstructure analysis
  LOM
  SEM
Statistical analysis
  Grain size
  Aspect ratio
  Slope
Grain packing & volume filling
  Packing-Algorithm e.g. RSA
  Tessellation e.g. Voronoi
Building the FE model
  Generating geometries
  Meshing geometries

## Slide 4: Microstructure Measurement
Ferrit 79%
Martensit 21%

## Slide 5: DRAGen – The Main Idea
Microstructure analysis
  LOM
  SEM
Statistical analysis
  Grain size
  Aspect ratio
  Slope
Grain packing & volume filling
  Packing-Algorithm e.g. RSA
  Tessellation e.g. Voronoi
Building the FE model
  Generating geometries
  Meshing geometries

## Slide 6: Input Data – Using a csv-File
from analysis of EBSD pictures via MATLAB toolbox MTEX,
command grains.fitEllipse
.csv files as input:
a in rolling direction, aligned with x-axis; b with y-axis and c with z-axis
Header: | a | b | c | alpha | phi1 | PHI | phi2
Description: | grain radius | grain radius | grain radius | grain slope x-y-plane | euler angle | euler angle | euler angle
Required: | mandatory | optional | optional | optional | optional | optional | optional
Default: |  | a | a | 0 | random | random | random
[1]
[1]: MTEX Documentation. https://mtex-toolbox.github.io/EllipseBasedParameters.html (last accessed: 10.05.2021)

## Slide 7: Input Data – Rotation & Texture
Slope
implemented via slope alpha for each grain
slope alpha relative to x-axis (radius a, RD)
counterclockwise rotation in x-y-plane
default: alpha = 0°
Texture
implemented via the three euler angles phi1, PHI, phi2 for each grain (default: random texture)
information stored in the output file for the crystal plasticity model grainsdata.inp
x*
y*
alpha
y
x
z
default: alpha = 0°
alpha = 30°

## Slide 8: Input Data – Using Machine Learning
Trainingsdaten aus EBSD-Messungen

## Slide 9: Input Data – Using Machine Learning
Generator
z
Synthetische Daten
Real Daten
Diskriminator
Labels
Wasserstein-Loss
Wasserstein-Loss
Currently only supported in development mode please approach Niklas for further information

## Slide 10: DRAGen – The Main Idea
Microstructure analysis
  LOM
  SEM
Statistical analysis
  Grain size
  Aspect ratio
  Slope
Grain packing & volume filling
  Packing-Algorithm e.g. RSA
  Tessellation e.g. Voronoi
Building the FE model
  Generating geometries
  Meshing geometries

## Slide 11: The Generation Process – Why Ellipsoids?
RSA for spheres: Check if is satisfied for all combination of spheres
Spheres don‘t describe grainshapes suitable Ellipsoids are far more suitable

## Slide 12: The Generation Process – Generating the Grid
Phase 1 – Read input:
  Input data is read
  Total volume is discretized and converted to numpy array
  Ellipsoids from input are discretized and converted to numpy array
Phase 2 – RSA-Algorithm:
  Numpy array is randomly filled with ellipsoids starting with biggest
  Intersections are forbidden
Phase 3 – Tesselation-Algorithm:
  Ellipsoids grow with weighted speed
  If maximum volume of an ellipsoid is reached growth stops
Numpy array is kept periodic during the complete process

## Slide 13: The Generation Process – Generating the Grid
Phase 1 – Read input:
  Input data is read
  Total volume is discretized and converted to numpy array
  Ellipsoids from input are discretized and converted to numpy array
Phase 2 – RSA-Algorithm:
  Numpy array is randomly filled with ellipsoids starting with biggest
  Intersections are forbidden
Phase 3 – Tesselation-Algorithm:
  Ellipsoids grow with weighted speed
  If maximum volume of an ellipsoid is reached growth stops
Numpy array is kept periodic during the complete process

## Slide 14: The Generation Process – Generating the Grid
Phase 1 – Read input:
  Input data is read
  Total volume is discretized and converted to numpy array
  Ellipsoids from input are discretized and converted to numpy array
Phase 2 – RSA-Algorithm:
  Numpy array is randomly filled with ellipsoids starting with biggest
  Intersections are forbidden
Phase 3 – Tesselation-Algorithm:
  Ellipsoids grow with weighted speed
  If maximum volume of an ellipsoid is reached growth stops
Numpy array is kept periodic during the complete process

## Slide 15: DRAGen – The Main Idea
Microstructure analysis
  LOM
  SEM
Statistical analysis
  Grain size
  Aspect ratio
  Slope
Grain packing & volume filling
  Packing-Algorithm e.g. RSA
  Tessellation e.g. Voronoi
Building the FE model
  Generating geometries
  Meshing geometries

## Slide 16: The Generation Process – Building the Model
Use a spectral solver
Convert points into an FE-mesh with smoothing algorithm

## Slide 17: The Generation Process – Building the Model
where
and
Source: http://graphics.stanford.edu/courses/cs468-12-spring/LectureSlides/06_smoothing.pdf

## Slide 18: The Generation Process – Building the Model

## Slide 19: RVE-Development

## Slide 20: DRAGen – The Main Idea
Microstructure analysis
  LOM
  SEM
Statistical analysis
  Grain size
  Aspect ratio
  Slope
Grain packing & volume filling
  Packing-Algorithm e.g. RSA
  Tessellation e.g. Voronoi
Building the FE model
  Generating geometries
  Meshing geometries

## Slide 21: What‘s next?
CWGAN-GP for full statistically valid input generation
Export filter for DAMASK_spectral
New algorithm for band generation
Inclusions and substructures
Full support for 2D-RVE
Surface smoothing
For ideas, tips and suggestions please contact: DRAGen@iehk.rwth-aachen.de

## Slide 22: Access to DRAGen
Check out our Git Repository here